Remotely Operated Submersible Vehicle.

# Overview
The aim of this project is to design and build a remotely operated Submersible Vehicle, with a minimum dive depth of 3m. It will contain an video camera used to help control the vehicle.

The vehicle will be controlled by an operator from a distance. This will need to be a digital system, in order to reduce the complexity of multiplexing several signals over a single medium. The 2 options are USB and ethernet. As USB has a maximum cable length of 5m, ethernet is prefered. This will require some smart device to convert from USB to ethernet. A Raspberry PI could stream the camera, while also interfacing to an Arduino to control the vehicle.

The initial proof of concept project will consist of 2 parts:
Block Diagram Rev0 contains a list of all the sub components and how they interact.

Software components:
Camera Stream: Various programs and scripts to stream a USB web cam over a network, either using ffserver//ffmpeg and a web browser or SSH/GUVCVIEW through a terminal.

Control Program: Consists of an Arduino controlling several motors, a Uart to TCP conversion program, and a program to transmit control data from a joystick.

In the initial prototype there is no feed back about the battery condition.